## Slide 1: Suggested Arduino Development
Eric Sandoz
11/5/2014

## Slide 2
Brake Pressure Control
Brake Hydraulic Pressure Sensor
(0-5V analog)
Valve Coil FET
(0-12V PWM)
Valve Coil FET
(0-12V PWM)
Hydraulic Valve
(0-12V on/off)
Brake Cylinder
Main Hydraulic Pressure Control
Pump Hydraulic Pressure Sensor
(0-5V analog)
Pump Contactor
(0-12V on/off)
Hydraulic Pump
(12V)
Contactor FET
(0-12V on/off)
Steer Angle Control
Steer Angle Sensor
(0-5V PWM)
Valve Coil FET
(0-12V PWM)
Valve Coil FET
(0-12V PWM)
Hydraulic Valve
(0-12V on/off)
Steer Rotary Actuator
Lean Angle Control
Lean Angle Sensor
(0-5V PWM)
Valve Coil FET
(0-12V PWM)
Valve Coil FET
(0-12V PWM)
Hydraulic Valve
(0-12V on/off)
Lean Rotary Actuator
Human Machine Interface
Joystick HMI
- X,Y: 0-5V Analog
- 4 Buttons 0-5V Digital
Auxiliary Switches
- 4 Buttons 0-5V Digital
Traction Motor Control
Rear Wheel Speed Sensor
(0-5V PWM)
Motor Contactor
(0-12V on/off)
Traction Motor Controller (72V)
OpAmp
(0-5V Analog)
Traction Motor (72V)
DAC
(0-5V)
Contactor FET
(0-12V on/off)
Arduino Microcontroller
Description | Type | Qty
Input: Analog Voltage (0-5V) | Analog | 4
Input: PWM Input (0-5V) | PWM | 3
Input: Digital Switch | On/Off | 9
Output: FET Drive | On/Off | 2
Output: FET Current Drive | PWM | 6
Output: Analog Voltage (0-5V) | DAC | 1

## Slide 3: Suggested Arduino Hardware
Panucatt Azteeg X3 Pro (3D Printer Controller)
  Arduino Mega based (12 V, high current capable)
  Screw terminals makes wiring easy
  FETs for driving coils etc. already included
  Supports enough I/O for Dagne as is
    6 Analog Inputs
    2 Thermocouple Inputs
    8 PWM 12 V 20A outputs
    6 Digital Inputs
    1 high current FET (100A)
    SD Memory interface
    LCD Interface
    USB
    Breakout headers for more I/O
  http://www.panucatt.com/ProductDetails.asp?ProductCode=AX3pro
Can drive ViKi LCD for more HMI with Arduino libraries
  http://www.panucatt.com/product_p/vikilcd.htm
This will be the quickest way to get going, focusing on wiring and software and not circuits and soldering